## Slide 1
SHARP Content Distributor
for FlashAirTM
What is necessary before using this software?
June 2017
SHARP COPORATION
Ver.1.0

## Slide 2
Requirements
Prepare ①Device ②Monitor ③FlashAir ④Content
Support OS
Windows®/ Android/ iOS
Using browser to register contents in FlashAir.
Various types of OS supported.
*For more details, see operation manual.
①Device
Compute, tablet, or smartphone for use of SHARP Content Distributor for FlashAir
2

## Slide 3
Requirements
Support Model
PN-Y556
PN-Y496
PN-Y436
PN-Y326
②Monitor
Prepare ①Device ②Monitor ③FlashAir ④Content
3
③FlashAir
*Availability varies by country/region.
Support Model*
SD-WE series
(W-03)
as of May 2017
SD-WE032G
SD-WE016G
SD-WE008G

## Slide 4
Requirements
Prepare ①Device ②Monitor ③FlashAir ④Content
4
Support format
Still image : jpg
Video : wmv
*Still images and videos cannot be displayed at the same time.
④Content

## Slide 5
1. Settings of monitor
Operation Flow
5

## Slide 6
6
Insert FlashAir into the LCD monitor.

## Slide 7
7
Set [NO SIGNAL AUTO INPUT SELECT] to [ON].

## Slide 8
8
Set [AUTO PLAY] to [PHOTO] or [MOVIE].

## Slide 9
9
Set [THERMAL SENSOR SETTING] to installed direction.

## Slide 10
10
Set [POWER SAVE MODE] to [ON].

## Slide 11
Operation Flow
1. Settings of monitor
2. Register Contents
11

## Slide 12
Connect the device to FlashAir via wireless LAN.
SSID : FlashAirSharp
Password : 12341234
* The above SSID and Password are default settings.
12

## Slide 13
Using browser, connect to http://flashair/
13

## Slide 14
Add content (up to 30 files).
14

## Slide 15
Add content (up to 30 files).
15

## Slide 16
Delete unneeded connect.
16

## Slide 17
1
2
3
Specify the content display order.
17

## Slide 18
Content upload is completed.
18

## Slide 19
1. Settings of monitor
Operation Flow
Operation Flow
3. LCD monitor Off/On
1. Settings of monitor
2. Register Contents
19

## Slide 20
Turn the main power of LCD monitor [OFF]/[ON].
If you set [POWER SAVE MODE] to [ON], you can restart the monitor with the remote control.
20

## Slide 21
The content is displayed on the LCD monitor.
21

## Slide 22
Cautions
① Editing Content
A new content will be played after switching the main power of the LCD monitor [OFF]/[ON]. You can turn [OFF] and [ON] the LCD monitor with the remote control. Please distribute the content within a distance that the remote control can reach.
② Distribution of Content
The content is distributed via wireless LAN. The transmission speed depends on the environment such as using devices, FlashAir, etc.. The transmission speed may decrease, or be disabled to connect in some situations.
i.g. Obstacles, collision with other wireless devices, magnetic-field like a microwave, etc..
22

## Slide 23
Cautions
③ Switching Content (Still image / Video)
To display still images, use a remote control to set the LCD monitor
[SETUP] – [AUTO PLAY] – [PHOTO].
To display videos, use a remote control to set the LCD monitor [SETUP] – [AUTO PLAY] – [MOVIE].
④ [THERMAL SENSOR SETTING]
Please set the [THERMAL SENSOR SETTING] based on the actually installed direction of the LCD monitor.
[SETUP] – [THERMAL SENSOR SETTING] –
[LANDSCAPE] or [PORTRAIL] or [FACE UP] or [FACE DOWN].
23

## Slide 24
Cautions
⑤ FlashAir
The FlashAir is not included in the LCD monitor. Please procure it locally.
As to the latest supported version of FlashAir, please refer to the operation manual for the Setup tool.
Prior to use FlashAir initially, you need to add an application to FlashAir using the Setup tool. Extract “SetupTool_Cdist-forF_Vx.x.x.x.zip” to any folder, and insert FlashAir in your PC, then run the Setup tool (Cdist-SetupTool.exe).
If your FlashAir is not factory default settings, you need to format FlashAir by using format function, and then use the “FlashAir Software Update tool” to update the software. You can download the “FlashAir Software Update tool” from the following URL provided by Toshiba Corporation.
https://www.toshiba.co.jp/p-media/english/download/wl/updatetool_w03.htm
24

## Slide 25
FlashAir is a trademark of Toshiba Corporation. Windows is either a registered trademark or trademark of Microsoft Corporation in the US and/or other countries. Android is a trademark of Google Inc. IOS is a trademark or registered trademark of Cisco Systems, Inc. in the US and other countries and is used under license by Apple Inc. All other brand names and product names may be trademarks or registered trademarks of their respective owners. All screen images appearing in this document are simulated. Design and specifications are subject to change without prior notice.